## Slide 1: Programming of parallel systems
Shared memory systems

## Slide 2: What is a shared memory system
Single memory space accessible to the programmer
Processor communicate through the network to the memories
Might have one or multiple memory per processor [1]
If there is less memory than processor
  Memory contention
  All processor can write to the same memory at the same time
Notes: System where there is n processor
Whole space is accessible to the programmer
Processor communicate through the network
Might have one or multiple memory per processor
If there is less memory than processor, there will be contention

## Slide 3: Examples of shared memory system
Shared memory systems are popular because of their ease of use.
CPU
  Central processing unit
  Shares the main memory among many processor to provide a way for communication between threads.
GPU
  Graphics processing unit
  Typically runs hundreds to thousands of threads in parallel organized in SIMD blocks. [2]
    EX: ATI Radeon™ HD 4870 Architecture has 800 threads in 10 SIMD core [3]
Notes: Can be 16 multiprocessor with 80 thread each. Each thread does the same job
Called stream processing units for AMD

## Slide 4: Frameworks using shared memory for massively parallel systems
Due to the massive number of threads, applications have to be rewritten
OpenCL (Open Computing Language) [4]
  Royalty Free
  Originally developed by Apple, it was submitted to the non-profit Khronos Group
  Heterogeneous computing, same code run CPUs, GPUs and other
CUDA (Compute Unified Device Architecture)
  Proprietary to NVIDIA video cards
  Has an API to run OpenCL on CUDA
Notes: For massively parallel systems, it needs special frameworks to schedule thousand of threads.
On June 16, 2008 the Khronos Compute Working Group was formed.

## Slide 5: CUDA vs OpenCL
Feature | OpenCL | CUDA
C Language Support | Yes | Yes
CPU Support | Yes | No
License | Royalty Free | Proprietary
Community size | Medium | Large
Speed | Fast | Very fast
CUBLAS (math API) | no | yes
CUFFT (FFT API) | no | yes

## Slide 6: CUDA vs OpenCL - performance
[5]
[6]
Benchmarks were run using the same hardware and code

## Slide 7: GPU architecture

## Slide 8: CUDA memory types 1/2
Device memory – global memory
  shared
  large DDR5 memory (> 1GB)
  off-chip - no cache - slow
Texture cache
  opaque memory layout optimized for texture fetch [7]
  Free interpolation
  off-chip - cached
Notes: Talk about CUDA because there is a single design.
Texture cache size depend on the board, varies from 32KB to 1 MB

## Slide 9: CUDA memory types 2/2
Constant cache
  Off-chip
  Cached
  Slow
  Small (8KB)
Shared memory
  One per multiprocessor
  On-chip
  Fast (one clock cycle)
  Small (16KB)
  Can serve as a cache for the global memory
Notes: Constant data size = 64KB and the cache is 8KB

## Slide 10: Support for shared memory in hardware
Two types of shared memory
Global memory
  Shared among the multiprocessor
  No cache ... cache coherent
  Support for atomic operations
Shared memory
  Not a truly shared memory, because it is local to a multiprocessor
  Support for atomic operations
  Often serve a manual cache for the global memory
    The program explicitly write to the shared memory
    Private to a multiprocessor, shared between its threads

## Slide 11: Memory bandwidth 1/4
The memory is often the restricting factor in a system
Using a single bus and a single memory module restricts the system scalability [8]
  Only one processor could access the memory at one time
    Leads to serialization
Solution on the GPU:
  Use a LARGE memory bus width such as 384-bit. [9]
  This can lead to 48 byte read in parallel
  Use a hardware scheduler to send the right data to the right thread.
    There is no shuffling, first thread gets the first 4 byte, and so on.
    Software is responsible to read continuous data
Notes: Using a common, limited-bandwidth bus as an
interconnection network severely restricts system
scalability. Furthermore, this type of interconnection
network allows only one processor at a time to
communicate with the memory, leading to performance
degradation. To avoid this problem, the
shared memory is divided into memory modules, as
Figure 1 shows.

## Slide 12: Memory bandwidth 2/4
For a GeForce 480 GTX, theoretical scenario [9]
The Memory Bandwidth can be as high as 177.4 GB/sec
The performance can be as high as 1.35 Tflops
  1350 * 109 floating point operation per second
Float = 4 byte
Load 44.35 * 109 float/s
Process 1.35 * 1012 float/s
To have maximum utilisation we need
1,350 * 109 / 44.35 * 109 = 30.5 operations per memory access

## Slide 13: Memory bandwidth 3/4
In the GPU, the memory bandwidth is really high (177.4 GB/sec) and it is determined by the type of card
The bandwidth between the CPU and the GPU is limited by the communication link
  PCI-Express in most cases
    Max speed: 8GB/s
    Important to minimize the communication between the CPU and the GPU
Notes: The bandwidth between the CPU and the GPU is also important as it

## Slide 14: Memory bandwidth 4/4
In practice it is almost impossible to achieve maximum throughput because of the memory alignment requirements.
Solution: Shared memory
  Acts as a programmable cache
  It is possible to order the reads from the global memory and do the computation on a faster smaller memory

## Slide 15: Example of CUDA code
__global__ void example(float* A, float* B)
{
int i = threadIdx.x;
if (i > 0)
B[i] = S[i - 1];
}
int main()
{
float* A, * B;
cudaMalloc(&A, 1000);
cudaMalloc(&B, 1000);
example<<<1, 1000>>>(A, B);
}
Takes 3 second
Notes: Declares 2 array, and allocate memory on the GPU
In the real life we should populate the arrays
Calls a Kernel Times2 <<< >>> indicates it runs on the GPU
In times2
Declare an array of shared memory (max 16KB)
Gets the index for the thread, will be between 0 and 999
Copies from the global to the shared memory, will be optimized away and perform 384-bit load
Synchronize, to make sure the memory is all loaded
Add two values of the array and put them in B
Without the shared memory, it may be a lot slower.

## Slide 16: Code with shared memory
__global__ void example(float* A, float* B)
{
__shared__ float S[1000];
int i = threadIdx.x;
S[i] = A[i];
__syncthreads();
if (i > 0)
B[i] = S[i - 1];
}
int main()
{
float* A, * B;
cudaMalloc(&A, 1000);
cudaMalloc(&B, 1000);
example<<<1, 1000>>>(A, B);
}
Notes: Declares 2 array, and allocate memory on the GPU
In the real life we should populate the arrays
Calls a Kernel Times2 <<< >>> indicates it runs on the GPU
In times2
Declare an array of shared memory (max 16KB)
Gets the index for the thread, will be between 0 and 999
Copies from the global to the shared memory, will be optimized away and perform 384-bit load
Synchronize, to make sure the memory is all loaded
Add two values of the array and put them in B
Without the shared memory, it may be a lot slower.

## Slide 17: Example
I ran that simple program on my computer
Versus the simple solution without shared memory
GPU: GeForce 8800 GTS
 | Time (ms) | Load coalesced | Load uncoalesced
Shared memory | 325.6 | 9376 | 0
Global memory | 2965.98 | 0 | 298424
Notes: Yes, if we remove the S[i - 1] both methods are as fast.

## Slide 18: Explanation
2 load
32 load

## Slide 19
The state of the art graphics cards that have come out in April 2010 now use caches for global memory
  Two types of caches
    L2 cache shared between multiprocessors
      Cache-coherent
    L1 cache local to a multiprocessor
      Not cache-coherent

## Slide 20: Conclusion
CUDA vs OpenCL
  Fast, easy: CUDA
  Portable: OpenCL
Quick development
  Started in 2008
  Added a cache recently
Memory bandwidth limitations are major
  Use larger memory bus
  Use caching

## Slide 21: References
[1] Dandamudi, S.P.; , "Reducing run queue contention in shared memory multiprocessors," Computer , vol.30, no.3, pp.82-89, Mar 1997
doi: 10.1109/2.573673
URL: http://www.ieeexplore.ieee.org.proxy.bib.uottawa.ca/stamp/stamp.jsp?tp=&arnumber=573673&isnumber=12418
[2] http://developer.download.nvidia.com/compute/cuda/3_1/toolkit/docs/NVIDIA_CUDA_C_ProgrammingGuide_3.1.pdf
[3] http://developer.amd.com/gpu_assets/GPU%20Computing%20-%20Past%20Present%20and%20Future%20with%20ATI%20Stream%20Technology.pdf
[4] http://www.khronos.org/developers/library/overview/opencl_overview.pdf
[5] Weber, R.; Gothandaraman, A.; Hinde, R.; Peterson, G.; , "Comparing Hardware Accelerators in Scientific Applications: A Case Study," Parallel and Distributed Systems, IEEE Transactions on , vol.PP, no.99, pp.1-1, 0
doi: 10.1109/TPDS.2010.125
URL: http://www.ieeexplore.ieee.org.proxy.bib.uottawa.ca/stamp/stamp.jsp?tp=&arnumber=5482576&isnumber=4359390
[6] http://arxiv.org/abs/1005.2581v2
[7] http://www.math.ntu.edu.tw/~wwang/mtxcomp2010/download/cuda_04_ykhung.pdf
[8] Dandamudi, S.P.; , "Reducing run queue contention in shared memory multiprocessors," Computer , vol.30, no.3, pp.82-89, Mar 1997
doi: 10.1109/2.573673
URL: http://www.ieeexplore.ieee.org.proxy.bib.uottawa.ca/stamp/stamp.jsp?tp=&arnumber=573673&isnumber=12418
[9] http://www.nvidia.com/object/product_geforce_gtx_480_us.html

## Slide 22: Backup Slide

## Slide 25: http://www.realworldtech.com/page.cfm?ArticleID=RWT090808195242&p=3