## Slide 1: Excerpt from Interconnection Networks Computer Architecture: A Quantitative Approach 4th Edition, Appendix E
Timothy Mark Pinkston
University of Southern California
http://ceng.usc.edu/smart/slides/appendixE.html
José Duato
Universidad Politécnica de Valencia
http://www.gap.upv.es/slides/appendixE.html
…with major presentation contribution from José Flich, UPV
(and Cell BE EIB slides by Tom Ainsworth, USC)
Notes: This presentation is an excerpt (slides 51-57, 124-138) of the Appendix E of Computer Architecture: A Quantitative Approach.
The material covered here is an abstract model that can be applied to any type of network. Whether this be a LAN, WAN or a network of computer processors.
Some slides have been added to include specific inter-processor material.

## Slide 2: Outline
  E.1 Introduction (skipped)
  E.2 Interconnecting Two Devices (skipped)
  E.3 Interconnecting Many Devices
  E.4 Network Topology (skipped)
  E.5 Network Routing, Arbitration, and Switching
  E.6 Switch Microarchitecture (skipped)
  E.7 Practical Issues for Commercial Interconnection Networks (skipped)
  E.8 Examples of Interconnection Networks (skipped)
  E.9 Internetworking (skipped)
  E.10 Crosscutting Issues for Interconnection Networks (skipped)
  E.11 Fallacies and Pitfalls (skipped)
  E.12 Concluding Remarks and References
Notes: Only topics 3 and 5 are covered in this presentation.
Topic 3 will be of a quick overview of the basic concepts of interconnection networks.
Topic 5 is truncated to comprising only arbitration and switching. Routing concepts are covered in the second presentation.

## Slide 3: Interconnecting Many Devices
Node model for processors
Notes: The model of a node for multi-processor networks is very simply a routing unit connected to a standard processor. The L1 cache is the property of its processor while the L2 cache may or may not be shared in the network or neighbouring nodes. The number of such nodes included on a chip or system is usually high. For instance, the Intel TeraFLOPS architecture contains upwards of 80 processing elements on a single die.
This type of architecture is scalable from a single chip to multiple chip on a single board to entire supercomputers. However, communication becomes more complex and the routing overhead increases with the number of nodes.
The number of channels between nodes can vary greatly depending on the topology of the network as well as the number of nodes.

## Slide 4: Interconnecting Many Devices
Additional Network Structure and Functions
  Additional functions (routing, arbitration, switching)
    Routing
      Which of the possible paths are allowable (valid) for packets?
      Provides the set of operations needed to compute a valid path
      Executed at source, intermediate, or even at destination nodes
    Arbitration
      When are paths available for packets? (along with flow control)
      Resolves packets requesting the same resources at the same time
      For every arbitration, there is a winner and possibly many losers
        Losers are buffered (lossless) or dropped on overflow (lossy)
    Switching
      How are paths allocated to packets?
      The winning packet (from arbitration) proceeds towards destination
      Paths can be established one fragment at a time or in their entirety
Notes: The process of communications in a network can be divided into three disciplines:
Routing determines the path that will conduct packets from source to destination. This process must take into account traffic, path length as well as division of labor in calculating the route.
Arbitration resolves conflicts between multiple would-be owners of a given resource. This activity is similar to the traffic lights which protect drivers from colliding with other cars. Some arbitrators can actually drop packets (lossy) or store them in a buffer (lossless) which requires additional memory.
Switching is similar to routing; it must perform the task of configuring connection(s) in order to transmit packets. This is usually implemented with a cross-bar network.

## Slide 5: Interconnecting Many Devices
Shared-media Networks
  The network media is shared by all the devices
  Operation: half-duplex or full-duplex
Node
Node
Node
X
Notes: The simplest type of topology for interconnection network shares a single medium between each node. This setup features the absolute minimal amount of connections with n-1 lines (where n is the number of nodes).
One variation of shared-media is the ring topology where a loop is achieved and the number of nodes and connections is the same. This architecture allows for the looping around of packets which offers more flexibility than the “bus” architecture seen here.

## Slide 6: Interconnecting Many Devices
Shared-media Networks
  Arbitration
    Centralized arbiter for smaller distances between devices
      Dedicated control lines
    Distributed forms of arbiters
      CSMA/CD
        The device first checks the network (carrier sensing)
        Then checks if the data sent was garbled (collision detection)
        If collision, device must send data again (retransmission): wait an increasing exponential random amount of time beforehand
        Fairness is not guaranteed
      Token ring—provides fairness
        Owning the token provides permission to use network media
Node
Node
Node
token
holder
X
Notes: Due to the nature of Shared Media Networks, their arbitration is usually distributed. Each node must listen for traffic on its lines before it may transmit itself in order to avoid/reduce collisions. The most common protocol for such arbitration is “Carrier Sense” “Multiple Access” (CSMA) which has a few flavors:
CSMA/CD terminates a transmission as soon as a collision is detected thus reducing the probability of a second collision on retry.
CSMA/CA will wait a random amount of time before transmitting if the channel was previously busy.
There are also different types of “persistence” where the protocol is modified to use supervisor stations (o-persistent) or probability of transmission (p-persistent) depending on various factors.
The token ring protocol (only for ring topologies) only allows for one transmission at any given time over the network. The “token” allowing a node to be transmitting must be allocated using a fairness algorithm in order to prevent starvation and maximize network usage.

## Slide 7: Interconnecting Many Devices
Shared-media Networks
  Switching
    Switching is straightforward
    The granted device connects to the shared media
  Routing
    Routing is straightforward
    Performed at all the potential destinations
      Each end node device checks whether it is the target of the packet
    Broadcast and multicast is easy to implement
      Every end node devices sees the data sent on shared link anyway
  Established order: arbitration, switching, and then routing
Notes: Both switching and routing are trivial processes on a shared-media network. The switching is performed by each node which transmits when the arbitrator allows it. The routing is performed at each node which either consumes the packet if it is the intended recipient or passes it on to the next node.

## Slide 8: Interconnecting Many Devices
Switched-media Networks
  Disjoint portions of the media are shared via switching
  Switch fabric components
    Passive point-to-point links
    Active switches
      Dynamically establish communication between sets of source-destination pairs
  Aggregate bandwidth can be many times higher than that of shared-media networks
Node
Node
Node
Node
Switch
Fabric
Notes: The switched-media network allows for greater flexibility and bandwidth than its Shared-Media counterpart. A “switch fabric” made up of interconnected switches (cross-bars) links the nodes on the network. This architecture allows for a great variety of topologies and more flexibility over design. Because of their dynamic nature, switched-media networks are used when a great number of nodes are to be interconnected.

## Slide 9: Interconnecting Many Devices
Switched-media Networks
  Routing
    Every time a packet enters the network, it is routed
  Arbitration
    Centralized or distributed
    Resolves conflicts among concurrent requests
  Switching
    Once conflicts are resolved, the network “switches in” the required connections
  Established order: routing, arbitration, and then switching
Notes: For Shared-media networks, the process of communication is somewhat reversed. The paths are dynamically determined and thus routing takes precedence over arbitration and switching. Once the path has been determined either partially or completely, the router of a node must manage to send the packets over one of its connections while avoiding collisions (arbitration). This process can be centralized but is almost always distributed. The switches of the network then perform the duty of forming a path between destination and source nodes and deliver the packets.

## Slide 10: Interconnecting Many Devices
Comparison of Shared- versus Switched-media Networks
  Shared-media networks
    Low cost
    Aggregate network bandwidth does not scale with # of devices
    Global arbitration scheme required (a possible bottleneck)
    Time of flight increases with the number of end nodes
  Switched-media networks
    Aggregate network bandwidth scales with number of devices
    Concurrent communication
      Potentially much higher network effective bandwidth
    Beware: inefficient designs are quite possible
      Superlinear network cost but sublinear network effective bandwidth
Notes: Shared-media networks work best in a situation where there are few nodes to manage. While the bandwidth may be low, the process of switching and routing is very simple and do not add any overhead in performance. Arbitration however becomes more difficult and adds significant overhead as the number of nodes increases.
Switched-media networks are designed for large networks with complex topologies. The process of routing is thus much more complicated than for shared-media and is usually distributed in order to keep the network dynamic. This also provides for the possibility of dynamic paths which are calculated or modified at each node and can thus adapt to high traffic and disabled portions of the network. This architecture thus has a much larger bandwidth if implemented correctly. However, the overhead of routing can significantly slow things down if not done properly. Furthermore, the resources needed to create such a network are much higher than shared-media.

## Slide 11: Routing, Arbitration, and Switching
Arbitration
  Performed at each switch, regardless of topology
  Determines use of paths supplied to packets (When allocated?)
  Needed to resolve conflicts for shared resources by requestors
  Ideally:
    Maximize the matching between available network resources and packets requesting them
    At the switch level, arbiters maximize the matching of free switch output ports and packets located at switch input ports
  Problems:
    Starvation
      Arises when packets can never gain access to requested resources
      Solution: Grant resources to packets with fairness, even if prioritized
  Many straightforward distributed arbitration techniques for switches
    Two-phased arbiters, three-phased arbiters, and iterative arbiters
Notes: The process of arbitration is very similar regardless of architecture. The concern is to maximize the usage of resources (switches) while retaining fairness to all parties (packets). As always, collisions must be avoided.
There are many schemes for arbitration and a balance must be struck between the tradeoff of maximizing usage and minimizing overhead (the number of phases).

## Slide 12: Routing, Arbitration, and Switching
Two-phased arbiter
Arbitration
request phase
grant phase
Three-phased arbiter
request phase
grant phase
accept phase
Only two matches out of four requests
(50% matching)
Now, three matches out of four requests
(75% matching)
Optimizing the matching can increase r ( i.e., rA )
Notes: Two examples of arbitration schemes (green blocks are communicating, grays are denied access):
In two-phased arbitration, the requester makes a single demand for a resource and waits for an answer. If it is denied it must try again later; this is a serial process.
In three-phased arbiter, each requester may demand access from several arbiters and then choose which to use. This allows the process to be parallelized somewhat and will result in a higher rate of resource usage (lower rate of denials). The overhead is higher than two-phased arbitration however.

## Slide 13: Routing, Arbitration, and Switching
Switching
  Performed at each switch, regardless of topology
  Establishes the connection of paths for packets (How allocated?)
  Needed to increase utilization of shared resources in the network
  Ideally:
    Establish or “switch in” connections between network resources (1) only for as long as paths are needed and (2) exactly at the point in time they are ready and needed to be used by packets
    Allows for efficient use of network bandwidth to competing flows
  Switching techniques:
    Circuit switching
      pipelined circuit switching
    Packet switching
      Store-and-forward switching
      Cut-through switching: virtual cut-through and wormhole
Notes: Switching is the final process to be performed before packets can be transmitted. There are two options:
Circuit switching (similar to the telephone system) which reserves a path for the transmission of packets
Packet switching in which each packet may use a different path (not necessarily true for cut-through and wormhole) to its destination (no guarantees on the order either).

## Slide 14: Routing, Arbitration, and Switching
Switching
  Circuit switching
    A “circuit” path is established a priori and torn down after use
    Possible to pipeline the establishment of the circuit with the transmission of multiple successive packets along the circuit
      pipelined circuit switching
    Routing, arbitration, switching performed once for train of packets
      Routing bits not needed in each packet header
      Reduces latency and overhead
    Can be highly wasteful of scarce network bandwidth
      Links and switches go under utilized
        during path establishment and tear-down
        if no train of packets follows circuit set-up
Notes: In circuit switching, a token packet is sent first to reserve a path to its destination. This process must be completed before actual packets can complete their transit. However, packets may begin to transmit before the path is completely reserved in pipelined circuit switching.
Once the path has been determined, data flows unhindered from source to destination. However, all the resources are used up and unavailable to other processes regardless of the usage of the circuit. This is highly inefficient and can easily bring a well-connected network to its knees.

## Slide 15: Routing, Arbitration, and Switching
Switching
  Circuit switching
Source
end node
Destination
end node
Buffers
for “request”
tokens
Notes: Here is a simulation circuit switching. Our network consists of two nodes, three switches and a bus topology. In this first step the network is completely unused.

## Slide 16: Routing, Arbitration, and Switching
Request for circuit establishment
(routing and arbitration is performed during this step)
Switching
  Circuit switching
Source
end node
Destination
end node
Buffers
for “request”
tokens
Notes: The source node must send a packet. It determines the proper routing and arbitration before sending its request token down the line.

## Slide 17: Routing, Arbitration, and Switching
Request for circuit establishment
Switching
  Circuit switching
Source
end node
Destination
end node
Buffers
for “ack” tokens
Acknowledgment and circuit establishment
(as token travels back to the source, connections are established)
Notes: The request token has proceeded by each node to its destination and now returns to the source. After this is completed, the path will be configured and ready for transmission.

## Slide 18: Routing, Arbitration, and Switching
Request for circuit establishment
Switching
  Circuit switching
Source
end node
Destination
end node
Acknowledgment and circuit establishment
Packet transport
(neither routing nor arbitration is required)
Notes: The source node may now transmit packets as if it were directly connected to its destination.

## Slide 19: Routing, Arbitration, and Switching
HiRequest for circuit establishment
Switching
  Circuit switching
Source
end node
Destination
end node
Acknowledgment and circuit establishment
Packet transport
X
High contention, low utilization (r)  low throughput
Notes: The packets have been sent and the network is now locked down and no communications may occur to any of the three switches except for the pre-determined path.

## Slide 20: Routing, Arbitration, and Switching
Switching
  Packet switching
    Routing, arbitration, switching is performed on a per-packet basis
    Sharing of network link bandwidth is done on a per-packet basis
    More efficient sharing and use of network bandwidth by multiple flows if transmission of packets by individual sources is more intermittent
    Store-and-forward switching
      Bits of a packet are forwarded only after entire packet is first stored
      Packet transmission delay is multiplicative with hop count, d
    Cut-through switching
      Bits of a packet are forwarded once the header portion is received
      Packet transmission delay is additive with hop count, d
      Virtual cut-through: flow control is applied at the packet level
      Wormhole: flow control is applied at the flow unit (flit) level
      Buffered wormhole: flit-level flow control with centralized buffering
Notes: The more dynamic solution of packet switching provides a more efficient usage of resources at the cost of overhead. Every packet must be routed, arbitrated and switched independently of each other. This technique will result in higher bandwidth for intermittent communication. There are many flavors of packet switching:
Store-and-forward is the classic form where each packet is dealt with one at a time. Their path might be completely different and their order of arrival is not guaranteed. The work of routing, arbitration and switching is multiplied by the number of hops and is not re-used.
Cut-through switching is a hybrid between circuit and packet switching where “loose” paths are determined. Each node must keep buffer the information about the path instead of calculating it anew for every packet.

## Slide 21: Routing, Arbitration, and Switching
Switching
  Store-and-forward switching
Source
end node
Destination
end node
Packets are completely stored before any portion is forwarded
Store
Buffers
for data
packets
Notes: Here is a simulated store-and-forward situation. The packet is contained at the source node and is about to be sent.

## Slide 22: Routing, Arbitration, and Switching
Switching
  Store-and-forward switching
Source
end node
Destination
end node
Packets are completely stored before any portion is forwarded
Store
Forward
Requirement:
buffers must be
sized to hold
entire packet
(MTU)
Notes: The packet is received by the first node (completely). It will now perform its own routing, arbitration and switching before transmitting it to its neighbour. This process is repeated until the packet arrives at its destination.

## Slide 23: Routing, Arbitration, and Switching
Switching
  Cut-through switching
Source
end node
Destination
end node
Routing
Portions of a packet may be forwarded (“cut-through”) to the next switch
before the entire packet is stored at the current switch
Notes: The same situation viewed through cut-though switching. The packet is about to be sent and re-transmission can occur before the packet is completely received by the first switch. However, the header must be completely transmitted before re-transmission may occur. This header is kept at each switch and will be used to transmit the rest of the packet.

## Slide 24: Routing, Arbitration, and Switching
Switching
  Virtual cut-through
  Wormhole
Source
end node
Destination
end node
Source
end node
Destination
end node
Buffers for data
packets
Requirement:
buffers must be sized
to hold entire packet
(MTU)
Buffers for flits:
packets can be larger
than buffers
“Virtual Cut-Through: A New Computer Communication Switching Technique,” P. Kermani and L. Kleinrock,
Computer Networks, 3, pp. 267–286, January, 1979.
Notes: A comparison of virtual cut-through and wormhole:
Virtual cut-through begins transmission in the same way as normal cut-through and the entire packet will be buffered at a node if there is a busy link.
Wormhole distributes the packet among the intermediate nodes and thus saves up on buffer size. This however can become a very complicated situation as packets from multiple paths are fragmented and can lead to deadlocks.

## Slide 25: Routing, Arbitration, and Switching
Switching
  Virtual cut-through
  Wormhole
Source
end node
Destination
end node
Source
end node
Destination
end node
Busy
Link
Packet stored
along the path
Busy
Link
Packet completely
stored at
the switch
Maximizing sharing of link BW increases r ( i.e., rS )
Buffers for data
packets
Requirement:
buffers must be sized
to hold entire packet
(MTU)
Buffers for flits:
packets can be larger
than buffers
“Virtual Cut-Through: A New Computer Communication Switching Technique,” P. Kermani and L. Kleinrock,
Computer Networks, 3, pp. 267–286, January, 1979.
Notes: A busy link is encountered and the resource usage of the wormhole technique is much higher than virtual cut-through.

## Slide 26: Concluding Remarks and References
Agarwal, A. [1991]. “Limits on interconnection network performance,” IEEE Trans. on Parallel and Distributed Systems 2:4 (April), 398–412.
Anderson, T. E., D. E. Culler, and D. Patterson [1995]. “A case for NOW (networks of workstations),” IEEE Micro 15:1 (February), 54–64.
Anjan, K. V., and T. M. Pinkston [1995]. “An efficient, fully-adaptive deadlock recovery scheme: Disha,” Proc. 22nd Int’l Symposium on Computer Architecture (June), Italy.
Benes, V.E. [1962]. “Rearrangeable three stage connecting networks,” Bell System Technical Journal 41, 1481–1492.
Bertozzi, D., A. Jalabert, S. Murali, R. Tamhankar, S. Stergiou, L. Benini, and G. De Micheli [2005]. “NoC synthesis flow for customized domain specific multiprocessor systems-on-chip,” IEEE Trans. on Parallel and Distributed Systems 16:2 (February),113–130.
Bhuyan, L. N., and D. P. Agrawal [1984]. “Generalized hypercube and hyperbus structures for a computer network,” IEEE Trans. on Computers 32:4 (April), 323–333.
Clos, C. [1953]. “A study of non-blocking switching networks,” Bell Systems Technical Journal 32 (March), 406–424.
Dally, W. J. [1990]. “Performance analysis of k-ary n-cube interconnection networks,” IEEE Trans. on Computers 39:6 (June), 775–785.
Dally, W. J. [1992]. “Virtual channel flow control,” IEEE Trans. on Parallel and Distributed Systems 3:2 (March), 194–205.
References

## Slide 27: Concluding Remarks and References
Dally, W. J. [1999]. “Interconnect limited VLSI architecture,” Proc. of the International Interconnect Technology Conference, San Francisco (May).
Dally, W. J., and C. I. Seitz [1986]. “The torus routing chip,” Distributed Computing 1:4, 187–196.
Dally, W. J., and B. Towles [2001]. “Route packets, not wires: On-chip interconnection networks,” Proc. of the Design Automation Conference, Las Vegas (June).
Dally, W. J., and B. Towles [2004]. Principles and Practices of Interconnection Networks, Morgan Kaufmann Publishers, San Francisco.
Duato, J. [1993]. “A new theory of deadlock-free adaptive routing in wormhole networks,” IEEE Trans. on Parallel and Distributed Systems 4:12 (Dec.) 1320–1331.
Duato, J., I. Johnson, J. Flich, F. Naven, P. Garcia, T. Nachiondo [2005]. “A new scalable and cost-effective congestion management strategy for lossless multistage interconnection networks,” Proc. 11th Int’l Symposium on High Performance Computer Architecture (February), San Francisco.
Duato, J., O. Lysne, R. Pang, and T. M. Pinkston [2005]. “Part I: A theory for deadlock-free dynamic reconfiguration of interconnection networks,” IEEE Trans. on Parallel and Distributed Systems 16:5 (May), 412–427.
Duato, J., and T. M. Pinkston [2001]. “A general theory for deadlock-free adaptive routing using a mixed set of resources,” IEEE Trans. on Parallel and Distributed Systems 12:12 (December), 1219–1235.
Duato, J., S. Yalamanchili, and L. Ni [2003]. Interconnection Networks: An Engineering Approach, 2nd printing, Morgan Kaufmann Publishers, San Francisco.
References

## Slide 28: Concluding Remarks and References
Glass, C. J., and L. M. Ni [1992]. “The Turn Model for adaptive routing,” Proc. 19th Int’l Symposium on Computer Architecture (May), Australia.
Gunther, K. D. [1981]. “Prevention of deadlocks in packet-switched data transport systems,” IEEE Trans. on Communications COM–29:4 (April), 512–524.
Ho, R., K. W. Mai, and M. A. Horowitz [2001]. “The future of wires,” Proc. of the IEEE 89:4 (April), 490–504.
Holt, R. C. [1972]. “Some deadlock properties of computer systems,” ACM Computer Surveys 4:3 (September), 179–196.
Infiniband Trade Association [2001]. InfiniBand Architecture Specifications Release 1.0.a, www.infinibandta.org.
Jantsch. A., and H. Tenhunen [2003]. Networks on Chips, eds., Kluwer Academic Publishers, The Netherlands.
Kermani, P., and L. Kleinrock [1979]. “Virtual Cut-Through: A New Computer Communication Switching Technique,” Computer Networks, 3 (January), 267–286.
Leiserson, C. E. [1985]. “Fat trees: Universal networks for hardware-efficient supercomputing,” IEEE Trans. on Computers C–34:10 (October), 892–901.
Merlin, P. M., and P. J. Schweitzer [1980]. “Deadlock avoidance in store-and-forward networks––I: Store-and-forward deadlock,” IEEE Trans. on Communications COM–28:3 (March), 345–354.
Metcalfe, R. M., and D. R. Boggs [1976]. “Ethernet: Distributed packet switching for local computer networks,” Comm. ACM 19:7 (July), 395–404.
References

## Slide 29: Concluding Remarks and References
Peh, L. S., and W. J. Dally [2001]. “A delay model and speculative architecture for pipelined routers,” Proc. 7th Int’l Symposium on High Performance Computer Architecture (January), Monterrey.
Pfister, Gregory F. [1998]. In Search of Clusters, 2nd ed., Prentice Hall, Upper Saddle River, N.J.
Pinkston, T. M. [2004]. “Deadlock characterization and resolution in interconnection networks (Chapter 13),” Deadlock Resolution in Computer-Integrated Systems, edited by M. C. Zhu and M. P. Fanti, Marcel Dekkar/CRC Press, 445–492.
Pinkston, T. M., A. Benner, M. Krause, I. Robinson, T. Sterling [2003]. “InfiniBand: The ‘de facto’ future standard for system and local area networks or just a scalable replacement for PCI buses?” Cluster Computing (Special Issue on Communication Architecture for Clusters) 6:2 (April), 95–104.
Pinkston, T. M., and J. Shin [2005]. “Trends toward on-chip networked microsystems,” International Journal of High Performance Computing and Networking 3:1, 3–18.
Pinkston, T. M., and S. Warnakulasuriya [1997]. “On deadlocks in interconnection networks,” Proc. 24th Int’l Symposium on Computer Architecture (June), Denver.
Puente, V., R. Beivide, J. A. Gregorio, J. M. Prellezo, J. Duato, and C. Izu [1999]. “Adaptive bubble router: A design to improve performance in torus networks,” Proc. 28th Int’l Conference on Parallel Processing (September), Aizu-Wakamatsu, Japan.
Saltzer, J. H., D. P. Reed, and D. D. Clark [1984]. “End-to-end arguments in system design,” ACM Trans. on Computer Systems 2:4 (November), 277–288.
References

## Slide 30: Concluding Remarks and References
Scott, S. L., and J. Goodman [1994]. “The impact of pipelined channels on k-ary n-cube networks ,” IEEE Trans. on Parallel and Distributed Systems 5:1 (January), 1–16.
Tamir, Y., and G. Frazier [1992]. “Dynamically-allocated multi-queue buffers for VLSI communication switches,” IEEE Trans. on Computers 41:6 (June), 725–734.
Taylor, M. B., W. Lee, S. P. Amarasinghe, and A. Agarwal [2005]. “Scalar operand networks,” IEEE Trans. on Parallel and Distributed Systems 16:2 (February), 145–162.
von Eicken, T., D. E. Culler, S. C. Goldstein, K. E. Schauser [1992]. “Active Messages: A mechanism for integrated communication and computation,”Proc. 19th Int’l Symposium on Computer Architecture (May), Australia.
Vaidya, A. S., A. Sivasubramaniam, and C. R. Das [1997]. “Performance benefits of virtual channels and adaptive routing: An application-driven study,” Proceedings of the 1997 Int’l Conference on Supercomputing (July), Austria.
Waingold, E., M. Taylor, D. Srikrishna, V. Sarkar, W. Lee, V. Lee, J. Kim, M. Frank, P. Finch, R. Barua, J. Babb, S. Amarasinghe, and A. Agarwal [1997]. “Baring it all to software: Raw Machines,” IEEE Computer, 30 (September), 86–93.
Yang, Y., and G. Mason [1991]. “Nonblocking broadcast switching networks,” IEEE Trans. on Computers 40:9 (September), 1005–1015.
References