## Slide 1: Adaptive Routing
David Ouellet-Poulin - 4073219
CEG 4136 – Computer Architecture III
November 16th, 2010

## Slide 2: Questions/Topics
Describe several algorithms used for adaptive routing.
Describe problems and advantages of these routing algorithms.
Which rely on routing table in each router?
What types of routing algorithms are used in multicore/multiprocessor system-on-chip?
Are adaptive algorithms used at all?

## Slide 3: Overview
Introduction
  Livelock
  Deadlock
Algorithms
  Turn Model
  Odd-Even Turn Model
  Planar
  GOAL
Example Systems
  IBMCell
  Intel TeraFLOPS
  Tilera TILE64
  ST Microelectronics STNoC

## Slide 4: Introduction
(1,1)
(1,2)
(1,3)
(1,4)
(2,1)
(2,2)
(2,3)
(2,4)
(3,1)
(3,2)
(3,3)
(3,4)
(4,1)
(4,2)
(4,3)
(4,4)
?
?
1 1 0 1 0 1 1 0 1 0 1 1
1 1 0 0 1 1 0 1 1 1 1 0
1 0 0 0 0 1 0 0 0 1 0 1
0 1 0 1 1 0 0 0 0 1 0 1
0 0 0 1 0 0 0 1 0 1 0 1
0 1 0 1 0 1 1 1 0 1 0 1
0 1 0 1 0 1 0 1 0 1 0 1

## Slide 5: Introduction – LiveLock [3]
(1,1)
(1,2)
(1,3)
(1,4)
(2,1)
(2,2)
(2,3)
(2,4)
(3,1)
(3,2)
(3,3)
(3,4)
(4,1)
(4,2)
(4,3)
(4,4)

## Slide 6: Introduction
Introduction – DeadLock [3]
(1,1)
(1,2)
(1,3)
(1,4)
(2,1)
(2,2)
(2,3)
(2,4)
(3,1)
(3,2)
(3,3)
(3,4)
(4,1)
(4,2)
(4,3)
(4,4)
(4,3)

## Slide 7: Algorithms - Turn Model [1]
3 modes:
  West First Turns:
  North Last Turns:
  Negative First Turns:

## Slide 8: Algorithms - Turn Model [1]
Partition the channels in the network into sets according to the directions in which they route packets. If each node has v channels in a physical direction, treat these channels as being in v distinct virtual directions and divide them into v distinct sets accordingly. Put any wraparound channels (for tori) in a separate set to be incorporated during Step 5.
Identify the possible turns from one virtual direction to another, ignoring 180-degree and 0-degree turns. A 0-degree turn is only possible when there are multiple channels in one direction. It represents a transition from one set of channels to another when the two sets route packets in the same physical direction, but different virtual directions.
Identify the cycles that these abstract turns can form. Generally, identifying the simplest cycles in each plane of the topology is adequate.
Prohibit one turn in each abstract cycle so as to prevent deadlock. The turns must be chosen carefully in order to break every possible cycle, including complex cycles not identified in Step 3. A useful approach is first to break the cycles in each plane and then to check whether this allows more complex cycles.
Incorporate as many turns as possible from the set of wraparound channels, without reintroducing cycles. At least one turn for each wraparound channel can always be incorporated.
Incorporate as many 180-degree and 0-degree turns as possible, without reintroducing cycles.

## Slide 9: Algorithms - Turn Model [1]
Advantages
  Deadlock free
  Livelock free
  Does not require Routing Table
  Does not require extra (virtual) channels
Disadvantages
  Router must determine correct type
  Can easily lead to non-optimal routes (prohibits certain turns)
  Complex router logic
  Low level of adaptiveness (only partially adaptive)

## Slide 10: Algorithms – Odd-Even Turn Model [4]
Evolution of Turn Model
Restricts locations where certain turns can occur:
  Rule 1: Any packet is not allowed to take an EN turn at any nodes located in an even column, and it is not allowed to take an NW turn at any nodes located in an odd column.
  Rule 2: Any packet is not allowed to take an ES turn at any nodes located in an even column, and it is not allowed to take an SW turn at any nodes located in an odd column.
Deadlock free as long as 180-degree turns are prohibited

## Slide 11: Algorithms – Odd-Even Turn Model [4]
Advantages
  Does not require Routing Table
  More routing adaptiveness than standard turn model
  Improved communication performance under non-uniform traffic
  Does not prohibit turns in general
Disadvantages
  Cannot perform 180-degree turns
  Fault tolerance implementation not yet determined

## Slide 12: Algorithms - Planar-Adaptive [2]
Fully-adaptive in higher-dimensions
Minimal (never moves away from destination)
Constrains dimensions for routing:
Planar routing can use any path (not adaptive)
a
b
a
b

## Slide 13: Algorithms - Planar-Adaptive [2]
Advantages
  Deadlock free
  Simplifies routing within high-dimensional networks
  Simple logic
  Minimal
  No Routing Table
Disadvantages
    Requires extra (virtual) channels
    Only improvement in non-planar networks
    Planar routing not adaptive

## Slide 14: Algorithms – GOAL [6]
Globally Oblivious Adaptive Locally
Oblivious choice of direction (quadrants)
Focus on balancing load in each quadrant (on a torus)
Minimal routing in quadrant

## Slide 15: Algorithms – GOAL [6]
Advantages
  Deadlock free
  Livelock free
  Very little routing logic
Disadvantages
  Requires Routing Tables
  Requires extra (virtual) channels
  Deadlock free depends on number of virtual channels
  Only for Torus topology
  Non-minimal

## Slide 16: Example Systems – IBM Cell [6]
8 SIMD “Synergistic Processing Elements”
Interconnected Ring Topology
Oblivious
Simple choice of Left and Right
Maximum bisection width of > 300 GBytes/s

## Slide 17: Example Systems – Intel TeraFLOPS [6]
Research prototype with 80 PE’s
5 possible connections at each node
Source routing (supports up to 10 hops)
Flexible: can be oblivious, deterministic or even adaptive
Achieves 20 GigaFLOPS and max bisection bandwidth of 320 GBytes/s

## Slide 18: Example Systems – Tilera TILE64 [6]
64 PE’s
Real-time processing oriented
4 meshes of 16 nodes each (UDN, IDN, MDN, TDN)
Static networking with pre-set routing (circuit switching)

## Slide 19: Example Systems – STNoC [6]
Prototype architecture
“Ring-like” topology
Source routing
Not deadlock-free

## Slide 20: Conclusion
Adaptive routing algorithms are good for large number of PE’s
Can easily avoid deadlocks & livelocks
Complex logic is prohibitive
Not used extensively

## Slide 21: References
[1] Glass, C.J.; Ni, M.N.; , “The turn model for adaptive routing”, Proceedings of the International Symposium on Computer Architecture, pp. 278–287, May 1992
[2] Chien, A.A.; Kim, J.H.; , “Planar-adaptive routing: low-cost adaptive networks for multiprocessors”, Proceedings of the International Symposium on Computer Architecture, pp. 268-277, 1992
[3] Dally, W.J.; Aoki, H.; , "Deadlock-free adaptive routing in multicomputer networks using virtual channels“, Parallel and Distributed Systems, IEEE Transactions on , vol.4, no.4, pp.466-475, Apr 1993

## Slide 22: References
[4] Ge-Ming Chiu; , "The odd-even turn model for adaptive routing," Parallel and Distributed Systems, IEEE Transactions on , vol.11, no.7, pp.729-738, Jul 2000
[5] Arjun Singh; Dally, W.J.; Gupta, A.K.; Towles, B.; , "GOAL: a load-balanced adaptive routing algorithm for torus networks“, Computer Architecture, 2003. Proceedings. 30th Annual International Symposium on , vol., no., pp. 194- 205, 9-11 June 2003
[6] Jerger, N.E.; Peh, L.S.; , “On-Chip Networks”, Synthesis Lectures on Computer Architecture, vol. 4, no. 1, pp 1-141, 2009