## Slide 1: UML State Machines
Used to model the dynamic behaviour of a process
  Can be used to model a high level behaviour of an entire system
  Can be used to model the detailed behaviour of a single object
  All other possible levels of detail in between these extremes is also possible

## Slide 2: UML State Machine Example
Example of a garage door state machine
(We will come back to this example later)

## Slide 3: States
Symbol for a state
A system in a state will remain in it until the occurrence of an event that will cause it to transition to another one
  Being in a state means that a system will behave in a predetermined way in response to a given event
Symbols for the initial and final states

## Slide 4: States
Numerous types of events can cause the system to transition from one state to another
In every state, the system behaves in a different matter
Names for states are usually chosen as:
  Adjectives: open, closed, ready…
  Present continuous verbs: opening, closing, waiting…

## Slide 5: Transitions
Transitions are represented with arrows

## Slide 6: Transitions
Transitions represent a change in a state in response to an event
  Theoretically, it is supposed to occur in a instantaneous manner (it does not take time to execute)
A transition can have”
  Trigger: causes the transition; can be an event of simply the passage of time
  Guard: a condition that must evaluate to true for the transition to occur
  Effect: an action that will be invoked directly on the system of the object being modeled (if we are modeling an object, the effect would correspond to a specific method)

## Slide 7: State Actions
An effect can also be associated with a state
If a destination state is associated with numerous incident transitions (transitions arriving a that state), and every transition defines the same effect:
  The effect can therefore be associated with the state instead of the transitions (avoid duplications)
  This can be achieved using an “On Entry” effect (we can have multiple entry effects)
  We can also add one or more “On Exit” effect

## Slide 8: Self Transition
State can also have self transitions
  These self transition are more useful when they have an effect associated with them
Timer events are usually popular with self transitions
Below is a typical example:

## Slide 9: Coming back to Our Initial Example
Example of a garage door state machine

## Slide 10: Decisions
Just like activity diagrams, we can use decisions nodes (although we usually call them decision pseudo-states)
Decision pseudo-states are represented with a diamond
  We always have one input transition and multiple outputs
  The branch of execution is decided by the guards associated with the transitions coming out of the decision pseudo-state

## Slide 11: Decisions

## Slide 12: Compound States
A state machine can include several sub-machines
Below is an example of a sub-machine included in the compound state “Connected”
Connected
Waiting
ProcessingByte
receiveByte
byteProcessed
disconnect
Disconnected
connect
closeSession

## Slide 13: Compound States Example

## Slide 14: Compound States Example
Same example, with an alternative notation
  The link symbol in the “Check Pin” state indicates that the details of the sub-machine associated with “Check Pin” are specified in an another state machine

## Slide 15: Alternative Entry Points
Sometimes, in a sub-machine, we do not want to start the execution from the initial state
  We want to start the execution from a “name alternative entry point”
PerformActivity

## Slide 16: Alternative Entry Points
Here’s the same system, from a higher level
  Transition from the “No Already Initialized” state leads to the standard initial state in the sub-machine
  Transition from the “Already Initialized” state is connected to the named alternative entry point “Skip Initializing”

## Slide 17: Alternative Exit Points
It is also possible to have alternative exit points for a compound state
  Transition from “Processing Instructions” state takes the regular exit
  Transition from the “Reading Instructions” state takes an "alternative named exit point

## Slide 18: Use Case – Validate PIN (1)
Use case name: Validate PIN
Summary: System validates customer PIN
Actor: ATM Customer
Precondition: ATM is idle, displaying a Welcome message.

## Slide 19: Use Case – Validate PIN (2)
Main sequence:
  Customer inserts the ATM card into the card reader.
  If system recognizes the card, it reads the card number.
  System prompts customer for PIN.
  Customer enters PIN.
  System checks the card's expiration date and whether the card has been reported as lost or stolen.
  If card is valid, system then checks whether the user-entered PIN matches the card PIN maintained by the system.
  If PIN numbers match, system checks what accounts are accessible with the ATM card.
  System displays customer accounts and prompts customer for transaction type: withdrawal, query, or transfer.

## Slide 20: Use Case – Validate PIN (3)
Alternative sequences:
Step 2: If the system does not recognize the card, the system ejects the card.
Step 5: If the system determines that the card date has expired, the system confiscates the card.
Step 5: If the system determines that the card has been reported lost or stolen, the system confiscates the card.
Step 7: If the customer-entered PIN does not match the PIN number for this card, the system re-prompts for the PIN.
Step 7: If the customer enters the incorrect PIN three times, the system confiscates the card.
Steps 4-8: If the customer enters Cancel, the system cancels the transaction and ejects the card.
Postcondition: Customer PIN has been validated.

## Slide 21: ATM Machine Example
Validate PIN:

## Slide 22: ATM Machine Example
Funds withdrawal:

## Slide 23: Section 4
Behavioral Modeling

## Slide 24: Topics
We will continue to talk about UML State Machine
We will go through a complete example of a simple software construction case study with emphasis on UML State Machines
End this section with some final words of wisdom!

## Slide 25: Last Lecture
We have talked about UML State Machines
  States and transitions
  State effects
  Self Transition
  Decision pseudo-states
  Compound states
  Alternative entry and exit points
Today, we will tackle more advanced UML State Machines Concepts

## Slide 26: History States
A state machine describes the dynamic aspects of a process whose current behavior depends on its past
A state machine in effect specifies the legal ordering of states a process may go through during its lifetime
When a transition enters a compound state, the action of the nested state machine starts over again at its initial state
  Unless an alternative entry point is specified
There are times you'd like to model a process so that it remembers the last substate that was active prior to leaving the compound state

## Slide 27: History States
Simple washing machine state diagram:
  Power Cut event: transition to the “Power Off” state
  Restore Power event: transition to the active state before the power was cut off to proceed in the cycle

## Slide 28: Concurrent Regions
Sequential sub state machines are the most common kind of sub machines
  In certain modeling situations, concurrent sub machines might be needed (two or more sub state machines executing in parallel)
Brakes example:

## Slide 29: Concurrent Regions
Example of modeling system maintenance using concurrent regions
Idle
Maintenance
Testing devices
Self diagnosing
Waiting
Processing Command
Testing
Commanding
command
commandProcessed
[continue]
commandProcessed
[not continue]
maintain
diagnosisCompleted
testingCompleted
shutDown

## Slide 30: Orthogonal Regions
Concurrent Regions are also called Orthogonal Regions
These regions allow us to model a relationship of “And” between states (as opposed to the default “or” relationship)
  This means that in a sub state machine, the system can be in several states simultaneously
Let us analyse this phenomenon using an example of computer keyboard state machine

## Slide 31: Keyboard Example (1)
Keyboard example without Orthogonal Regions

## Slide 32: Keyboard Example (2)
Keyboard example with Orthogonal Regions

## Slide 33: Garage Door – Case Study
Background
  Company DOORS inc. manufactures garage door components
  Nonetheless, they have been struggling with the embedded software running on their automated garage opener Motor Unit that they developed in house
    This is causing them to loose business
  They decided to scrap the existing software and hire a professional software company to deliver “bug free” software

## Slide 34: Client Requirements
Client (informal) requirements:
  Requirement 1: When the garage door is closed, it must open whenever the user presses on the button of the wall mounted door control or the remote control
  Requirement 2: When the garage door is open, it must close whenever the user presses on the button of the wall mounted door control or the remote control
  Requirement 3: The garage door should not close on an obstacle
  Requirement 4: There should be a way to leave the garage door half open
  Requirement 5: System should run a self diagnosis test before performing any command (open or close) to make sure all components are functional

## Slide 35: Client Requirements
Motor Unit
(includes a microcontroller where the software will be running)
Wall Mounted Controller
(a remote controller is also supported)
Sensor Unit(s)
(detects obstacles, when the door is fully open and when it is fully closed)

## Slide 36: Use Case Diagram
Open Door
Close Door
Run Diagnosis
Use Case Diagram
include
include
Garage Door User
Garage Door System

## Slide 37: Run Diagnosis Use Case
Use Case Name: Run Diagnosis
Summary: The system runs a self diagnosis procedure
Actor: Garage door user
Pre-Condition: User has pressed the remote or wall mounted control button
Sequence:
  Check if the sensor is operating correctly
  Check if the motor unit is operating correctly
  If all checks are successful, system authorizes the command to be executed
Alternative Sequence:
Step 3: One of the checks fails and therefore the system does not authorize the execution of the command
Postcondition: Self diagnosis ensured that the system is operational

## Slide 38: Open Door Use Case
Use Case Name: Open Door
Summary: Open the garage the door
Actor: Garage door user
Dependency: Include Run Diagnosis use case
Pre-Condition: Garage door system is operational and ready to take a command
Sequence:
  User presses the remote or wall mounted control button
  Include Run Diagnosis use case
  If the door is currently closing or is already closed, system opens the door
Alternative Sequence:
Step 3: If the door is open, system closes door
Step 3: If the door is currently opening, system stops the door (leaving it half open)
Postcondition: Garage door is open

## Slide 39: Close Door Use Case
Use Case Name: Close Door
Summary: Close the garage the door
Actor: Garage door user
Dependency: Include Run Diagnosis use case
Pre-Condition: Garage door system is operational and ready to take a command
Sequence:
  User presses the remote or wall mounted control button
  Include Run Diagnosis use case
  If the door is currently open, system closes the door
Alternative Sequence:
Step 3: If the door is currently closing or is already closed, system opens the door
Step 3: If the door is currently opening, system stops the door (leaving it half open)
Postcondition: Garage door is closed

## Slide 40: High Level Behavioral Modeling

## Slide 41: High Level Structural Model

## Slide 42: Refined Structural Model

## Slide 43: Refine Behavioral Model – Motor Unit
buttonPressed(),
obstacleDetected()
[isFunctioning()]
Open
Closing
Closed
Opening
HalfOpen
buttonPressed()
buttonPressed()
buttonPressed() [isFunctioning()]
doorOpen()
doorClosed()
buttonPressed() [isFunctioning()]
Running
WaitingForRepair
buttonPressed(),
[! isFunctioning()]
Timer (180 s)
[! isFunctioning()]
Timer (180 s)
[isFunctioning()]

## Slide 44: Refine Behavioral Model – Sensor Unit
CheckingForObstacles
CheckingIfDoorOpen
CheckingIfDoorClosed
[!isObstacleDetected()]
[isObstacleDetected()]
[!isDoorOpen()]
[isDoorOpen()]
Sleeping
[!isDoorClosed()]
[isDoorClosed()]
Time (20 ms)
SendingObstacleEvent
SendingOpenDoorEvent
SendingDoorClosedEvent

## Slide 45: Do Not Fall Asleep yet!

## Slide 46: Coding
Whenever we are satisfied with the level of detail in our behavioral models, we can proceed to coding
Some of the code can be generated directly by tools from the behavioral model
  Some tweaking might be necessary (do not use the code blindly)
  Humans are still the smartest programmers

## Slide 47: Event Generator Class

## Slide 48: Sensor Class

## Slide 49: Sensor Class
Sensor
State machine Implementation

## Slide 50: Umple Online Demo
UMPLE is a modeling tool to enable what we call Model-Oriented Programming
  This is what we do in this course
You can use it to create class diagrams (structural models) and state machines (behavioral models)
The tool was developed at the university of Ottawa
  Online version can be found at:
  http://cruise.eecs.uottawa.ca/umpleonline/
  There’s also an eclipse plugin for the tool

## Slide 51: Umple Code For Motor Unit State Machine
class Motor {
  status {
    Running {
      Open {buttonPressed[isFunctioning()]->Closing; }
      Closing { buttonPressed()[isFunctioning()]->Opening;
        ObstacleDetected()[isFunctioning()]->Opening;
        doorClosed()->Closed;}
      Closed { buttonPressed()[isFunctioning()]->Opening; }
      Opening { buttonPressed()->HalfOpen;
        doorOpen()->Open; }
      HalfOpen{buttonPressed()->Opening;}
      buttonPressed()[!isFunctioning()]->WaitingForRepair;
  }
  WaitingForRepair{
      timer()[!isFunctioning()]->WaitingForRepair;
      timer()[isFunctioning()]->Running;}
  }
}

## Slide 52: Motor Class Snippets
Switching between high level states
Switching between nest states inside the Running compound state

## Slide 53: When To Use State Machines?
When an object or a system progresses through various stages of execution (states)
  The behavior of the system differs from one stage to another
When you can identify clear events that change the status of the system
They are ideal for event driven programming (less loops and branches, more events generated and exchanged)
  Lots of event are being exchanged between objects
When using even driven programming
  Make sure you follow Observable or Event Notifier patterns
  Both are pretty simple (similar to what we have done for the garage door example)

## Slide 54: Behavioral Over-Modeling
Please model responsibly!!
Do not get carried out with modeling every single detail to the point where you run behind schedule
  You sell code, not models…

## Slide 55: Behavioral Over-Modeling
Now, be careful, you do not want over-model
  Modern software development processes are all about only doing just enough modeling for a successful product
Therefore, start with a high level model of the behavior
  This model should give a clear overview of some (not necessary all) of the important functionality of the system
  This would be similar to the first garage door state machine we created

## Slide 56: Behavioral Over-Modeling
Identify potential complex areas that require further understanding
  We minimize the risk if we understand these components well before we start programing
  Model these complex areas in more details until you are satisfied that they are well understood
Use tools to generate code from your existing models
  Do not rely blindly on tools (at least not yet!)

## Slide 57: Designing Classes with State Diagrams
Keep the state diagram simple
  State diagrams can very quickly become extremely complex and confusing
  At all time, you should follow the aesthetic rule: “Less is More”
If the state diagram gets too complex consider splitting it into smaller classes
Think about compound states instead of a flat design

## Slide 58: Example of a CD Player with a Radio
On
Displaying Current Time
Displaying Alarm Time
Display Alarm
Timer (3 s)
Playing Radio
Playing CD
off
Off
On
H
On
Play CD
Play Radio

## Slide 59: More UML State Machines Examples
Flight State Machine

## Slide 60: More UML State Machines Examples
Flight State Machine Nested